How to repair Dimmer Chanel

1. Some channels stay on, doesn’t off (Other channels working fine)

Method to fix：

- SEE: Check the resistors of the channel (R6,R11..). If it’s burned or the color of the parts changed color. If yes, then replace the resistors.

- DIM4C3A BOTTOM PCBA Resistor location：

Channel 1： R6

Channel 2： R11

Channel 3： R13

Channel 4： R17

Material list：

| Parts series | Name & description | Unit | Qty | Remark |
| --- | --- | --- | --- | --- |
| RES00047 | 470Ω/1W±1% metal film resistor | pc | 4 | R6 R11 R17 R13 |

- DIM8C1A BOTTOM PCBA Resistor location：

Channel 1：R9

Channel 2： R11

Channel 3： R13

Channel 4： R15

Channel 5： R17

Channel 6： R19

Channel 7： R8

Channel 8： R10

Material list：

| Parts series | Name & description | Unit | Qty | Remark |
| --- | --- | --- | --- | --- |
| RES00047 | 470Ω/1W±1% metal film resistor | pc | 8 | R9,R10,R11,R13,R14,R15,R17,R19 |

- MIX24 BOTTOM PCBA Resistor location：

Channel 1： R12

Channel 2： R23

Channel 3： R20

Channel 4： R16

Material list：

| Parts series | Name & description | Unit | Qty | Remark |
| --- | --- | --- | --- | --- |
| RES00047 | 470Ω/1W±1% metal film resistor | pc | 4 | R12 16 20 23 |

- MIX23 BOTTOM PCBA Resistor location：

Channel 1： R12

Channel 2： R20

Channel 3： R16

Material list：

| Parts series | Name & description | Unit | Qty | Remark |
| --- | --- | --- | --- | --- |
| RES00047 | 470Ω/1W±1% metal film resistor | pc | 3 | R12 16 20 |

Photos：

- Dimmer channels flicker

Soldering again or replace resistor as below

- MIX23 BOTTOM PCBA Resistor location：

Channel 1： R13

Channel 2： R21

Channel 3： R17

Material list：

| Parts series | Name & description | Unit | Qty | Remark |
| --- | --- | --- | --- | --- |
| RES00046 | 39Ω/0.5W±1% metal film resistor | pc | 3 | R13 17 21 |